## Slide 1: Clock and temperature reading project
Omnia Nabil 12020156
Sohaila Mohammad Kandil 120200062

## Slide 2: Temperature sensing code The Clock code Layered architecture 01 02 TABLE OF CONTENTS 03

## Slide 3: Project description
In this project we display the temperature continuously on an LCD and each second the new time in hours, minutes and seconds is displayed on the LCD

## Slide 5: The layered architecture
The layered architecture helps in making the code well organized and user friendly.

## Slide 6: Defining the basic registers operations
These functions are called the macro definitions and they do the basic operations on registers

## Slide 7: Defining some data types

## Slide 8: MCAL

## Slide 9: DIO_types.h file
Defining all the channels names ,data directions, pins numbers, ports names. Makes the codes user friendly and makes it easier to debug the code if we use another microcontroller.

## Slide 10: DIO.h file
In this file we define all the digital input output functions we will implement in dio.c file

## Slide 11: DIO.config.h file
In this code we define a structure that can hold the port name, the pin number and the data direction either input or output.

## Slide 12: DIO.config.c file
In this file we made a list with elements of some structs that holds each register and pin and the information of whether this pin is set as an input or an output pin

## Slide 13: DIO.c file
The dio_init() function is setting the DDRX registers to settle the configurations for all pins if they are output or inputs

## Slide 14: DIO.c file
The dio_write() function is writing a specific value to a channel in the microcontroller.

## Slide 15: DIO.c file
The dio_read() function is reading a specific value from a channel in the microcontroller.

## Slide 16: HAL

## Slide 17: LCD configuration

## Slide 18: LCD.h file
Here we define all the functions we need for the lcd

## Slide 19: LCD.h file
Here we define all the commands we need for the lcd.

## Slide 20: LCD_config.h file
Here we set the pins configurations of the lcd.

## Slide 21: LCD.c file
In the init function we set the lcd to the initial stage to make it ready to display images

## Slide 22: Application layer

## Slide 23: Main.c file
In this piece of code we set the timer registers and set the interrupt on.

## Slide 24: Main.c file
In this piece of code the code is reading the temperature but sense we have called the init_timer1() function, once a second has passed the interrupt service routine will be called.
ADC_READ() functiion read the value from the temperature sensor and saves in variable temperature.

## Slide 25: The ISR of the clock

## Slide 26: The ISR of the clock

## Slide 27: The ISR of the clock
Finally at the ISR make sure to reset the TCNT registers for the coming interrupt.

## Slide 29: ADC_READ
starts a while loop that continues until the value of the ADC Interrupt Flag (ADIF) bit in the ADCSRA register becomes 1. It waits for the ADC conversion to finish.
combines the lower 8 bits (low_adc_bits) and the upper 2 bits (high_adc_bits) of the ADC result to form a 10-bit ADC reading. It then performs some scaling or calibration operation on the ADC reading and assigns the result to the variable ADC_read_val.

## Slide 30: Main and print_temp_lcd
the temperature variable take value from ADC_READ.
pass to function print_temp_lcd
to show the temperature value on lcd.
Start on line 1 position 0 in lcd

## Slide 31: THANKS